## Slide 1: KBE app to support the design of automotive rear spoilers Knowledge Acquisition
Group 40
Bas v. Manen & Stijn Nolet

## Slide 2: “Knowledge” for parametric model of high-performance spoiler design is taken from existing spoiler designs
Rear spoiler function is to generate downforce
Simple, robust model consists of
  Upside down wing
  Connector struts
  Optional endplates

## Slide 4: Aerodynamic analysis: AVL
AVL is used to calculate:
  Lift distribution
  Lift-induced drag distribution
  Total lift and total lift induced drag

## Slide 5: Aerodynamic analysis: Parasite drag
Parasite drag calculated with
  Reynolds number
  Form factor
  Wetted area
  Frontal area

## Slide 6: Aerodynamic analysis: XFOIL
XFOIL is used to calculate sectional pressure distribution
Investigate effect of spoiler angle on sectional downforce coefficient

## Slide 7: Structural analysis: sectional properties
Calculate along the spoiler (for inputted t)
  Cross sectional area
  Centroid position
  Moments of inertia

## Slide 8: Structural analysis: bending calculations
The spoiler is modelled as a beam using the Euler-Bernouli beam theory.
Bending and shear is calculated using the methods described in Megson.

## Slide 9: Structural analysis: stress calculations
The normal stress due to bending
Shear stress due to bending

## Slide 10: Structural analysis: Failure modes
Tensile stress yielding
Shear stress yielding
Compressive stress skin buckling and shear stress buckling

## Slide 11: Structural analysis: Failure modes cont.
Compressive stress column buckling
Max deflection > 5% of half span

## Slide 12: Bibliography
Engineering Mechanics Statics, 14th edition, R.C. Hibbeler.
Aircraft structures for engineering students, 5th edition, T.H.G. Megson.