## Slide 1: KBE app to support the design of automotive rear spoilers Knowledge Acquisition
Group 40
Bas v. Manen & Stijn Nolet

## Slide 2: “Knowledge” for parametric model of high-performance spoiler design is taken from existing spoiler designs
Rear spoiler function is to generate downforce
Simple, robust model consists of
  Upside down wing
  Connector struts
  Optional endplates

## Slide 3: Part identification
Endplate
Main plate
Strut

## Slide 4: Part identification (2)
Main plate (1 … *)
  Main source of downforce, airfoil shape
Struts (2 … *)
  Can be either airfoil shaped or flat plate
Endplates
  Can be either present or not, acting like winglets
Car model
  Based on existing high-performance vehicles

## Slide 5: Aerodynamic analysis: Parasite drag
Parasite drag calculated with
  Reynolds number
  Form factor
  Wetted area
  Frontal area

## Slide 6: Aerodynamic analysis: AVL
AVL is used to calculate:
  Lift distribution
  Lift-induced drag distribution
  Total lift and total lift induced drag

## Slide 7: Aerodynamic analysis: XFOIL
XFOIL is used to calculate sectional pressure distribution
Investigate effect of spoiler angle on sectional downforce coefficient

## Slide 8: Structural analysis: sectional properties
Calculate along the spoiler (for inputted t)
  Cross sectional area
  Centroid position
  Moments of inertia

## Slide 9: Structural analysis: bending calculations
The spoiler is modelled as a beam using the Euler-Bernouli beam theory.
Bending and shear is calculated using the methods described in Megson.

## Slide 10: Structural analysis: stress calculations
The normal stress due to bending
Shear stress due to bending

## Slide 11: Structural analysis: Failure modes
Tensile stress yielding
Shear stress yielding
Compressive stress skin buckling and shear stress buckling

## Slide 12: Structural analysis: Failure modes cont.
Compressive stress column buckling
Max deflection > 5% of half span

## Slide 13: Bibliography
Engineering Mechanics Statics, 14th edition, R.C. Hibbeler.
Aircraft structures for engineering students, 5th edition, T.H.G. Megson.
Advanced Aircraft Design (2013), Egbert Torenbeek
Technical Regulations for Grand Touring Cars, FIA Sport / Technical Department, 2020.